## Slide 1: Computer Architecture Lecture 14: SIMD Processors and GPUs
Dr. Juan Gómez Luna
Prof. Onur Mutlu
ETH Zürich
Fall 2019
8 November 2019

## Slide 2: Agenda for This Lecture
SIMD Processing
  Vector and Array Processors
Graphics Processing Units (GPUs)

## Slide 3: Exploiting Data Parallelism: SIMD Processors and GPUs

## Slide 4: SIMD Processing: Exploiting Regular (Data) Parallelism

## Slide 5: Flynn’s Taxonomy of Computers
Mike Flynn, “Very High-Speed Computing Systems,” Proc. of IEEE, 1966
SISD: Single instruction operates on single data element
SIMD: Single instruction operates on multiple data elements
  Array processor
  Vector processor
MISD: Multiple instructions operate on single data element
  Closest form: systolic array processor, streaming processor
MIMD: Multiple instructions operate on multiple data elements (multiple instruction streams)
  Multiprocessor
  Multithreaded processor

## Slide 6: Data Parallelism
Concurrency arises from performing the same operation on different pieces of data
  Single instruction multiple data (SIMD)
  E.g., dot product of two vectors
Contrast with data flow
  Concurrency arises from executing different operations in parallel (in a data driven manner)
Contrast with thread (“control”) parallelism
  Concurrency arises from executing different threads of control in parallel
SIMD exploits operation-level parallelism on different data
  Same operation concurrently applied to different pieces of data
  A form of ILP where instruction happens to be the same across data

## Slide 7: SIMD Processing
Single instruction operates on multiple data elements
  In time or in space
Multiple processing elements
Time-space duality
  Array processor: Instruction operates on multiple data elements at the same time using different spaces
  Vector processor: Instruction operates on multiple data elements in consecutive time steps using the same space

## Slide 8: Array vs. Vector Processors
ARRAY PROCESSOR
VECTOR PROCESSOR
LD VR  A[3:0]
ADD VR  VR, 1
MUL VR  VR, 2
ST A[3:0]  VR
Instruction Stream
Time
LD0
LD1
LD2
LD3
AD0
AD1
AD2
AD3
MU0
MU1
MU2
MU3
ST0
ST1
ST2
ST3
LD0
LD1
AD0
LD2
AD1
MU0
LD3
AD2
MU1
ST0
AD3
MU2
ST1
MU3
ST2
ST3
Space
Space
Same op @ same time
Different ops @ same space
Different ops @ time
Same op @ space

## Slide 9: SIMD Array Processing vs. VLIW
VLIW: Multiple independent operations packed together by the compiler

## Slide 10: SIMD Array Processing vs. VLIW
Array processor: Single operation on multiple (different) data elements

## Slide 11: Vector Processors (I)
A vector is a one-dimensional array of numbers
Many scientific/commercial programs use vectors
    for (i = 0; i<=49; i++)
    C[i] = (A[i] + B[i]) / 2
A vector processor is one whose instructions operate on vectors rather than scalar (single data) values
Basic requirements
  Need to load/store vectors  vector registers (contain vectors)
  Need to operate on vectors of different lengths  vector length register (VLEN)
  Elements of a vector might be stored apart from each other in memory  vector stride register (VSTR)
    Stride: distance in memory between two elements of a vector

## Slide 12: Vector Processors (II)
A vector instruction performs an operation on each element in consecutive cycles
  Vector functional units are pipelined
  Each pipeline stage operates on a different data element
Vector instructions allow deeper pipelines
  No intra-vector dependencies  no hardware interlocking needed within a vector
  No control flow within a vector
  Known stride allows easy address calculation for all vector elements
    Enables prefetching of vectors into registers/cache/memory

## Slide 13: Vector Processor Advantages
+ No dependencies within a vector
  Pipelining & parallelization work really well
  Can have very deep pipelines, no dependencies!
+ Each instruction generates a lot of work
  Reduces instruction fetch bandwidth requirements
+ Highly regular memory access pattern
+ No need to explicitly code loops
  Fewer branches in the instruction sequence

## Slide 14: Vector Processor Disadvantages
-- Works (only) if parallelism is regular (data/SIMD parallelism)
++ Vector operations
-- Very inefficient if parallelism is irregular
-- How about searching for a key in a linked list?
Fisher, “Very Long Instruction Word architectures and the ELI-512,” ISCA 1983.

## Slide 15: Vector Processor Limitations
-- Memory (bandwidth) can easily become a bottleneck, especially if
1. compute/memory operation balance is not maintained
2. data is not mapped appropriately to memory banks

## Slide 16: Vector Processing in More Depth

## Slide 17: Vector Registers
Each vector data register holds N M-bit values
Vector control registers: VLEN, VSTR, VMASK
Maximum VLEN can be N
  Maximum number of elements stored in a vector register
Vector Mask Register (VMASK)
  Indicates which elements of vector to operate on
  Set by vector test instructions
    e.g., VMASK[i] = (Vk[i] == 0)
V0,0
V0,1
V0,N-1
V1,0
V1,1
V1,N-1
M-bit wide
M-bit wide

## Slide 18: Vector Functional Units
Use a deep pipeline to execute element operations
   fast clock cycle
Control of deep pipeline is simple because elements in vector are independent
V1
V2
V3
V1 * V2  V3
Six stage multiply pipeline
Slide credit: Krste Asanovic

## Slide 19: Vector Machine Organization (CRAY-1)
CRAY-1
Russell, “The CRAY-1 computer system,” CACM 1978.
Scalar and vector modes
8 64-element vector registers
64 bits per element
16 memory banks
8 64-bit scalar registers
8 24-bit address registers

## Slide 20: CRAY X-MP-28 @ ETH (CAB, E Floor)

## Slide 21: CRAY X-MP System Organization
Cray Research Inc., “The CRAY X-MP Series of Computer Systems,” 1985

## Slide 22: CRAY X-MP Design Detail
Cray Research Inc., “The CRAY X-MP Series of Computer Systems,” 1985

## Slide 23: CRAY X-MP CPU Functional Units
Cray Research Inc., “The CRAY X-MP Series of Computer Systems,” 1985

## Slide 24: CRAY X-MP System Configuration
Cray Research Inc., “The CRAY X-MP Series of Computer Systems,” 1985

## Slide 25: Seymour Cray, the Father of Supercomputers
"If you were plowing a field, which would you rather use: Two strong oxen or 1024 chickens?"
© amityrebecca / Pinterest. https://www.pinterest.ch/pin/473018767088408061/
© Scott Sinklier / Corbis. http://america.aljazeera.com/articles/2015/2/20/the-short-brutal-life-of-male-chickens.html

## Slide 26: Vector Machine Organization (CRAY-1)
CRAY-1
Russell, “The CRAY-1 computer system,” CACM 1978.
Scalar and vector modes
8 64-element vector registers
64 bits per element
16 memory banks
8 64-bit scalar registers
8 24-bit address registers

## Slide 27: Loading/Storing Vectors from/to Memory
Requires loading/storing multiple elements
Elements separated from each other by a constant distance (stride)
  Assume stride = 1 for now
Elements can be loaded in consecutive cycles if we can start the load of one element per cycle
  Can sustain a throughput of one element per cycle
Question: How do we achieve this with a memory that takes more than 1 cycle to access?
Answer: Bank the memory; interleave the elements across banks

## Slide 28: Memory Banking
Memory is divided into banks that can be accessed independently; banks share address and data buses (to minimize pin cost)
Can start and complete one bank access per cycle
Can sustain N parallel accesses if all N go to different banks
Bank
0
Bank
1
MDR
MAR
Bank
2
Bank
15
MDR
MAR
MDR
MAR
MDR
MAR
Data bus
Address bus
CPU
Picture credit: Derek Chiou

## Slide 29: Vector Memory System
Next address = Previous address + Stride
If (stride == 1) && (consecutive elements interleaved across banks) && (number of banks >= bank latency), then
  we can sustain 1 element/cycle throughput
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
+
Base
Stride
Vector Registers
Memory Banks
Address Generator
Picture credit: Krste Asanovic

## Slide 30: Scalar Code Example: Element-Wise Avg.
For I = 0 to 49
  C[i] = (A[i] + B[i]) / 2
Scalar code (instruction and its latency)
  MOVI R0 = 50 1
  MOVA R1 = A 1
  MOVA R2 = B 1
  MOVA R3 = C 1
  X: LD R4 = MEM[R1++] 11 ;autoincrement addressing
  LD R5 = MEM[R2++] 11
  ADD R6 = R4 + R5 4
  SHFR R7 = R6 >> 1 1
  ST MEM[R3++] = R7 11
  DECBNZ R0, X 2 ;decrement and branch if NZ
304 dynamic instructions

## Slide 31: Scalar Code Execution Time (In Order)
Scalar execution time on an in-order processor with 1 bank
  First two loads in the loop cannot be pipelined: 2*11 cycles
  4 + 50*40 = 2004 cycles
Scalar execution time on an in-order processor with 16 banks (word-interleaved: consecutive words are stored in consecutive banks)
  First two loads in the loop can be pipelined
  4 + 50*30 = 1504 cycles
Why 16 banks?
  11-cycle memory access latency
  Having 16 (>11) banks ensures there are enough banks to overlap enough memory operations to cover memory latency

## Slide 32: Vectorizable Loops
A loop is vectorizable if each iteration is independent of any other
For I = 0 to 49
  C[i] = (A[i] + B[i]) / 2
Vectorized loop (each instruction and its latency):
  MOVI VLEN = 50 1
  MOVI VSTR = 1 1
  VLD V0 = A 11 + VLEN – 1
  VLD V1 = B 11 + VLEN – 1
  VADD V2 = V0 + V1 4 + VLEN – 1
  VSHFR V3 = V2 >> 1 1 + VLEN – 1
  VST C = V3 11 + VLEN – 1
7 dynamic instructions

## Slide 33: Basic Vector Code Performance
Assume no chaining (no vector data forwarding)
  i.e., output of a vector functional unit cannot be used as the direct input of another
  The entire vector register needs to be ready before any element of it can be used as part of another operation
One memory port (one address generator)
16 memory banks (word-interleaved)
285 cycles

## Slide 34: Vector Chaining
Vector chaining: Data forwarding from one vector functional unit to another
Memory
V1
Load Unit
Mult.
V2
V3
Chain
Add
V4
V5
Chain
LV v1
MULV v3,v1,v2
ADDV v5, v3, v4
Slide credit: Krste Asanovic

## Slide 35: Vector Code Performance - Chaining
Vector chaining: Data forwarding from one vector functional unit to another
182 cycles
These two VLDs cannot be
pipelined. WHY?
VLD and VST cannot be
pipelined. WHY?
Strict assumption:
Each memory bank
has a single port
(memory bandwidth
bottleneck)

## Slide 36: Vector Code Performance – Multiple Memory Ports
Chaining and 2 load ports, 1 store port in each bank
79 cycles
19X perf. improvement!

## Slide 37: Questions (I)
What if # data elements > # elements in a vector register?
  Idea: Break loops so that each iteration operates on # elements in a vector register
    E.g., 527 data elements, 64-element VREGs
    8 iterations where VLEN = 64
    1 iteration where VLEN = 15 (need to change value of VLEN)
  Called vector stripmining

## Slide 38: (Vector) Stripmining
Source: https://en.wikipedia.org/wiki/Surface_mining

## Slide 39: Questions (II)
What if vector data is not stored in a strided fashion in memory? (irregular memory access to a vector)
  Idea: Use indirection to combine/pack elements into vector registers
  Called scatter/gather operations

## Slide 40: Gather/Scatter Operations
Want to vectorize loops with indirect accesses:
  for (i=0; i<N; i++)
  A[i] = B[i] + C[D[i]]
Indexed load instruction (Gather)
  LV vD, rD # Load indices in D vector
  LVI vC, rC, vD # Load indirect from rC base
  LV vB, rB # Load B vector
  ADDV.D vA,vB,vC # Do add
  SV vA, rA # Store result
Notes: Gather example

## Slide 41: Gather/Scatter Operations
Gather/scatter operations often implemented in hardware to handle sparse vectors (matrices)
Vector loads and stores use an index vector which is added to the base register to generate the addresses
Scatter example
Index Vector Data Vector (to Store) Stored Vector (in Memory)
0 3.14 Base+0 3.14
2 6.5 Base+1 X
6 71.2 Base+2 6.5
7 2.71 Base+3 X
Base+4 X
Base+5 X
Base+6 71.2
Base+7 2.71
Notes: Scatter example

## Slide 42: Conditional Operations in a Loop
What if some operations should not be executed on a vector (based on a dynamically-determined condition)?
  loop: for (i=0; i<N; i++)
  if (a[i] != 0) then b[i]=a[i]*b[i]
Idea: Masked operations
  VMASK register is a bit mask determining which data element should not be acted upon
  VLD V0 = A
  VLD V1 = B
  VMASK = (V0 != 0)
  VMUL V1 = V0 * V1
  VST B = V1
  This is predicated execution. Execution is predicated on mask bit.

## Slide 43: Another Example with Masking
for (i = 0; i < 64; ++i)
if (a[i] >= b[i])
c[i] = a[i]
else
c[i] = b[i]
A B VMASK
1 2 0
2 2 1
3 2 1
4 10 0
-5 -4 0
0 -3 1
6 5 1
-7 -8 1
Steps to execute the loop in SIMD code
1. Compare A, B to get
VMASK
2. Masked store of A into C
3. Complement VMASK
4. Masked store of B into C

## Slide 44: Masked Vector Instructions
C[4]
C[5]
C[1]
Write data port
A[7]
B[7]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
Density-Time Implementation
  scan mask vector and only execute elements with non-zero masks
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
Write data port
Write Enable
A[7]
B[7]
M[7]=1
Simple Implementation
  execute all N operations, turn off result writeback according to mask
Slide credit: Krste Asanovic
Which one is better?
Tradeoffs?

## Slide 45: Some Issues
Stride and banking
  As long as they are relatively prime to each other and there are enough banks to cover bank access latency, we can sustain 1 element/cycle throughput
Storage of a matrix
  Row major: Consecutive elements in a row are laid out consecutively in memory
  Column major: Consecutive elements in a column are laid out consecutively in memory
  You need to change the stride when accessing a row versus column

## Slide 46: Matrix Multiplication
A and B, both in row-major order
A: Load A0 into vector register V1
  Each time, increment address by one to access the next column
  Accesses have a stride of 1
B: Load B0 into vector register V2
  Each time, increment address by 10
  Accesses have a stride of 10
A4x6 B6x10 → C4x10
Dot products of rows and columns of A and B
Different strides can lead to bank conflicts
How do we minimize them?

## Slide 47: Minimizing Bank Conflicts
More banks
Better data layout to match the access pattern
  Is this always possible?
Better mapping of address to bank
  E.g., randomized mapping
  Rau, “Pseudo-randomly interleaved memory,” ISCA 1991.

## Slide 48: Array vs. Vector Processors, Revisited
Array vs. vector processor distinction is a “purist’s” distinction
Most “modern” SIMD processors are a combination of both
  They exploit data parallelism in both time and space
  GPUs are a prime example we will cover in a bit more detail

## Slide 49: Recall: Array vs. Vector Processors
ARRAY PROCESSOR
VECTOR PROCESSOR
LD VR  A[3:0]
ADD VR  VR, 1
MUL VR  VR, 2
ST A[3:0]  VR
Instruction Stream
Time
LD0
LD1
LD2
LD3
AD0
AD1
AD2
AD3
MU0
MU1
MU2
MU3
ST0
ST1
ST2
ST3
LD0
LD1
AD0
LD2
AD1
MU0
LD3
AD2
MU1
ST0
AD3
MU2
ST1
MU3
ST2
ST3
Space
Space
Same op @ same time
Different ops @ same space
Different ops @ time
Same op @ space

## Slide 50: Vector Instruction Execution
VADD A,B  C
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
Execution using one pipelined functional unit
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
A[24]
B[24]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
A[25]
B[25]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
A[26]
B[26]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
A[27]
B[27]
Execution using four pipelined functional units
Slide credit: Krste Asanovic
Time
Space
Time

## Slide 51: Vector Unit Structure
Lane
Functional Unit
Partitioned
Vector
Registers
Memory Subsystem
Elements 0, 4, 8, …
Elements 1, 5, 9, …
Elements 2, 6, 10, …
Elements 3, 7, 11, …
Slide credit: Krste Asanovic

## Slide 52: Vector Instruction Level Parallelism
Can overlap execution of multiple vector instructions
  Example machine has 32 elements per vector register and 8 lanes
  Completes 24 operations/cycle while issuing 1 vector instruction/cycle
load
load
mul
mul
add
add
Load Unit
Multiply Unit
Add Unit
time
Instruction issue
Slide credit: Krste Asanovic

## Slide 53: Automatic Code Vectorization
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Vectorization is a compile-time reordering of operation sequencing
 requires extensive loop dependence analysis
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Time
Slide credit: Krste Asanovic

## Slide 54: Vector/SIMD Processing Summary
Vector/SIMD machines are good at exploiting regular data-level parallelism
  Same operation performed on many data elements
  Improve performance, simplify design (no intra-vector dependencies)
Performance improvement limited by vectorizability of code
  Scalar operations limit vector machine performance
  Remember Amdahl’s Law
  CRAY-1 was the fastest SCALAR machine at its time!
Many existing ISAs include (vector-like) SIMD operations
  Intel MMX/SSEn/AVX, PowerPC AltiVec, ARM Advanced SIMD

## Slide 55: SIMD Operations in Modern ISAs

## Slide 56: SIMD ISA Extensions
Single Instruction Multiple Data (SIMD) extension instructions
  Single instruction acts on multiple pieces of data at once
  Common application: graphics
  Perform short arithmetic operations (also called packed arithmetic)
For example: add four 8-bit numbers
Must modify ALU to eliminate carries between 8-bit values
56

## Slide 57: Intel Pentium MMX Operations
Idea: One instruction operates on multiple data elements simultaneously
  À la array processing (yet much more limited)
  Designed with multimedia (graphics) operations in mind
Peleg and Weiser, “MMX Technology
Extension to the Intel Architecture,”
IEEE Micro, 1996.
No VLEN register
Opcode determines data type:
8 8-bit bytes
4 16-bit words
2 32-bit doublewords
1 64-bit quadword
Stride is always equal to 1.

## Slide 58: MMX Example: Image Overlaying (I)
Goal: Overlay the human in image 1 on top of the background in image 2
Peleg and Weiser, “MMX Technology Extension to the Intel Architecture,” IEEE Micro, 1996.

## Slide 59: MMX Example: Image Overlaying (II)
Peleg and Weiser, “MMX Technology Extension to the Intel Architecture,” IEEE Micro, 1996.
Y = Blossom image
X = Woman’s image

## Slide 60: Fine-Grained Multithreading

## Slide 61: Fine-Grained Multithreading (I)
Idea: Hardware has multiple thread contexts (PC+registers). Each cycle, fetch engine fetches from a different thread.
  By the time the fetched branch/instruction resolves, no instruction is fetched from the same thread
  Branch/instruction resolution latency overlapped with execution of other threads’ instructions
+ No logic needed for handling control and
data dependences within a thread
-- Single thread performance suffers
-- Extra logic for keeping thread contexts
-- Does not overlap latency if not enough
threads to cover the whole pipeline
Notes: Latency overlap/hiding

## Slide 62: Fine-Grained Multithreading (II)
Idea: Switch to another thread every cycle such that no two instructions from a thread are in the pipeline concurrently
Tolerates the control and data dependency latencies by overlapping the latency with useful work from other threads
Improves pipeline utilization by taking advantage of multiple threads
  Thornton, “Parallel Operation in the Control Data 6600,” AFIPS 1964.
  Smith, “A pipelined, shared resource MIMD computer,” ICPP 1978.

## Slide 63: Multithreaded Pipeline Example
Slide credit: Joel Emer

## Slide 64: Fine-grained Multithreading (III)
Advantages
  + No need for dependency checking between instructions
  (only one instruction in pipeline from a single thread)
  + No need for branch prediction logic
  + Otherwise-bubble cycles used for executing useful instructions from different threads
  + Improved system throughput, latency tolerance, utilization
Disadvantages
  - Extra hardware complexity: multiple hardware contexts (PCs, register files, …), thread selection logic
  - Reduced single thread performance (one instruction fetched every N cycles from the same thread)
  - Resource contention between threads in caches and memory
  - Some dependency checking logic between threads remains (load/store)

## Slide 65: GPUs (Graphics Processing Units)

## Slide 66: GPUs are SIMD Engines Underneath
The instruction pipeline operates like a SIMD pipeline (e.g., an array processor)
However, the programming is done using threads, NOT SIMD instructions
To understand this, let’s go back to our parallelizable code example
But, before that, let’s distinguish between
  Programming Model (Software)
  vs.
  Execution Model (Hardware)

## Slide 67: Programming Model vs. Hardware Execution Model
Programming Model refers to how the programmer expresses the code
  E.g., Sequential (von Neumann), Data Parallel (SIMD), Dataflow, Multi-threaded (MIMD, SPMD), …
Execution Model refers to how the hardware executes the code underneath
  E.g., Out-of-order execution, Vector processor, Array processor, Dataflow processor, Multiprocessor, Multithreaded processor, …
Execution Model can be very different from the Programming Model
  E.g., von Neumann model implemented by an OoO processor
  E.g., SPMD model implemented by a SIMD processor (a GPU)

## Slide 68: How Can You Exploit Parallelism Here?
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Let’s examine three programming options to exploit instruction-level parallelism present in this sequential code:
1. Sequential (SISD)
2. Data-Parallel (SIMD)
3. Multithreaded (MIMD/SPMD)

## Slide 69: Prog. Model 1: Sequential (SISD)
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Can be executed on a:
Pipelined processor
Out-of-order execution processor
  Independent instructions executed when ready
  Different iterations are present in the instruction window and can execute in parallel in multiple functional units
  In other words, the loop is dynamically unrolled by the hardware
Superscalar or VLIW processor
  Can fetch and execute multiple instructions per cycle
for (i=0; i < N; i++)
C[i] = A[i] + B[i];

## Slide 70: Prog. Model 2: Data Parallel (SIMD)
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Realization: Each iteration is independent
Idea: Programmer or compiler generates a SIMD instruction to execute the same instruction from all iterations across different data
Best executed by a SIMD processor (vector, array)
VLD A  V1
VLD B  V2
VADD V1 + V2  V3
VST V3  C

## Slide 71: Prog. Model 3: Multithreaded
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Realization: Each iteration is independent
Idea: Programmer or compiler generates a thread to execute each iteration. Each thread does the same thing (but on different data)
Can be executed on a MIMD machine

## Slide 72: Prog. Model 3: Multithreaded
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Realization: Each iteration is independent
Idea: Programmer or compiler generates a thread to execute each iteration. Each thread does the same thing (but on different data)
Can be executed on a MIMD machine
This particular model is also called:
SPMD: Single Program Multiple Data
Can be executed on a SIMD machine
Can be executed on a SIMT machine
Single Instruction Multiple Thread

## Slide 73: A GPU is a SIMD (SIMT) Machine
Except it is not programmed using SIMD instructions
It is programmed using threads (SPMD programming model)
  Each thread executes the same code but operates a different piece of data
  Each thread has its own context (i.e., can be treated/restarted/executed independently)
A set of threads executing the same instruction are dynamically grouped into a warp (wavefront) by the hardware
  A warp is essentially a SIMD operation formed by hardware!

## Slide 74: SPMD on SIMT Machine
Warp 0 at PC X+3
Warp 0 at PC X+2
Warp 0 at PC X+1
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Realization: Each iteration is independent
Idea: Programmer or compiler generates a thread to execute each iteration. Each thread does the same thing (but on different data)
Can be executed on a MIMD machine
This particular model is also called:
SPMD: Single Program Multiple Data
Can be executed on a SIMD machine
A GPU executes it using the SIMT model:
Single Instruction Multiple Thread
Warp 0 at PC X
Warp: A set of threads that execute
the same instruction (i.e., at the same PC)

## Slide 75: Graphics Processing Units SIMD not Exposed to Programmer (SIMT)

## Slide 76: SIMD vs. SIMT Execution Model
SIMD: A single sequential instruction stream of SIMD instructions  each instruction specifies multiple data inputs
  [VLD, VLD, VADD, VST], VLEN
SIMT: Multiple instruction streams of scalar instructions  threads grouped dynamically into warps
  [LD, LD, ADD, ST], NumThreads
Two Major SIMT Advantages:
  Can treat each thread separately  i.e., can execute each thread independently (on any type of scalar pipeline)  MIMD processing
  Can group threads into warps flexibly  i.e., can group threads that are supposed to truly execute the same instruction  dynamically obtain and maximize benefits of SIMD processing

## Slide 77: Fine-Grained Multithreading of Warps
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Warp 0 at PC X
Assume a warp consists of 32 threads
If you have 32K iterations, and 1 iteration/thread  1K warps
Warps can be interleaved on the same pipeline  Fine grained multithreading of warps
Warp 1 at PC X
Iter. 33
Iter. 34
Warp 20 at PC X+2
Iter.
20*32 + 1
Iter.
20*32 + 2

## Slide 78: Warps and Warp-Level FGMT
Warp: A set of threads that execute the same instruction (on different data elements)  SIMT (Nvidia-speak)
All threads run the same code
Warp: The threads that run lengthwise in a woven fabric …
Thread Warp 3
Thread Warp 8
Thread Warp 7
Thread Warp
Scalar
Thread
W
Scalar
Thread
X
Scalar
Thread
Y
Scalar
Thread
Z
Common PC
SIMD Pipeline
Lindholm et al., "NVIDIA Tesla: A Unified Graphics and Computing Architecture," IEEE Micro 2008.
Notes: In SIMD, you need to specify the data array + an instruction (on which to operate the data on) + THE INSTRUCTION WIDTH. Eg: You might want to add 2 integer arrays of length 16, then a SIMD instruction would look like (the instruction has been cooked-up by me for demo) add.16 arr1 arr2 However, SIMT doesn't bother about the instruction width. So, essentially, you could write the above example as: arr1[i] + arr2[i] and then launch as many threads as the length of the array, as you want. Note that, if the array size was, let us say, 32, then SIMD EXPECTS you to explicitly call two such 'add.16' instructions! Whereas, this is not the case with SIMT.

## Slide 79: High-Level View of a GPU
Lindholm et al., "NVIDIA Tesla: A Unified Graphics and Computing Architecture," IEEE Micro 2008.

## Slide 80: Latency Hiding via Warp-Level FGMT
Warp: A set of threads that execute the same instruction (on different data elements)
Fine-grained multithreading
  One instruction per thread in pipeline at a time (No interlocking)
  Interleave warp execution to hide latencies
Register values of all threads stay in register file
FGMT enables long latency tolerance
  Millions of pixels
Decode
R
F
R
F
R
F
A
L
U
A
L
U
A
L
U
D-Cache
Thread Warp 6
Thread Warp 1
Thread Warp 2
Data
All Hit?
Miss?
Warps accessing
memory hierarchy
Thread Warp 3
Thread Warp 8
Writeback
Warps available
for scheduling
Thread Warp 7
I-Fetch
SIMD Pipeline
Slide credit: Tor Aamodt
Notes: With a large number of shader threads multiplexed on the same execution re- sources, our architecture employs fine-grained multithreading where individual threads are interleaved by the fetch unit to proactively hide the potential latency of stalls before they occur. As illustrated by Figure, warps are issued fairly in a round-robin queue. When a thread is blocked by a memory request, shader core simply removes that thread’s warp from the pool of “ready” warps and thereby allows other threads to proceed while the memory system processes its request.
With a large number of threads (1024 per shader core) interleaved on the same pipeline, FGMT effectively hides the latency of most memory operations since the pipeline is occupied with instructions from other threads while memory operations complete. also hides the pipeline latency so that data bypassing logic can potentially be omitted to save area with minimal impact on performance. simplify the dependency check logic design by restricting each thread to have at most one instruction running in the pipeline at any time.

## Slide 81: Warp Execution (Recall the Slide)
32-thread warp executing ADD A[tid],B[tid]  C[tid]
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
Execution using one pipelined functional unit
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
A[24]
B[24]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
A[25]
B[25]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
A[26]
B[26]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
A[27]
B[27]
Execution using four pipelined functional units
Slide credit: Krste Asanovic
Time
Space
Time

## Slide 82
Lane
Functional Unit
Registers
for each
Thread
Memory Subsystem
Registers for thread IDs
0, 4, 8, …
Registers for thread IDs
1, 5, 9, …
Registers for thread IDs
2, 6, 10, …
Registers for thread IDs
3, 7, 11, …
Slide credit: Krste Asanovic
SIMD Execution Unit Structure

## Slide 83: Warp Instruction Level Parallelism
Can overlap execution of multiple instructions
  Example machine has 32 threads per warp and 8 lanes
  Completes 24 operations/cycle while issuing 1 warp/cycle
W3
W0
W1
W4
W2
W5
Load Unit
Multiply Unit
Add Unit
time
Warp issue
Slide credit: Krste Asanovic

## Slide 84: SIMT Memory Access
Same instruction in different threads uses thread id to index and access different data elements
Let’s assume N=16, 4 threads per warp  4 warps
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
+
+
+
+
+
Slide credit: Hyesoon Kim
Threads
Data elements
Warp 0
Warp 1
Warp 2
Warp 3

## Slide 85: Warps not Exposed to GPU Programmers
CPU threads and GPU kernels
  Sequential or modestly parallel sections on CPU
  Massively parallel sections on GPU: Blocks of threads
Serial Code (host)
. . .
. . .
Parallel Kernel (device)
KernelA<<< nBlk, nThr >>>(args);
Serial Code (host)
Parallel Kernel (device)
KernelB<<< nBlk, nThr >>>(args);
Slide credit: Hwu & Kirk

## Slide 86: Sample GPU SIMT Code (Simplified)
for (ii = 0; ii < 100000; ++ii) {
C[ii] = A[ii] + B[ii];
}
// there are 100000 threads
__global__ void KernelFunction(…) {
int tid = blockDim.x * blockIdx.x + threadIdx.x;
int varA = aa[tid];
int varB = bb[tid];
C[tid] = varA + varB;
}
CPU code
CUDA code
Slide credit: Hyesoon Kim

## Slide 87: Sample GPU Program (Less Simplified)
Slide credit: Hyesoon Kim

## Slide 88: From Blocks to Warps
GPU cores: SIMD pipelines
  Streaming Multiprocessors (SM)
  Streaming Processors (SP)
Blocks are divided into warps
  SIMD unit (32 threads)
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 0’s warps
Block 1’s warps
…
t0 t1 t2 … t31
…
Block 2’s warps
NVIDIA Fermi architecture

## Slide 89: Warp-based SIMD vs. Traditional SIMD
Traditional SIMD contains a single thread
  Sequential instruction execution; lock-step operations in a SIMD instruction
  Programming model is SIMD (no extra threads)  SW needs to know vector length
  ISA contains vector/SIMD instructions
Warp-based SIMD consists of multiple scalar threads executing in a SIMD manner (i.e., same instruction executed by all threads)
  Does not have to be lock step
  Each thread can be treated individually (i.e., placed in a different warp)  programming model not SIMD
    SW does not need to know vector length
    Enables multithreading and flexible dynamic grouping of threads
  ISA is scalar  SIMD operations can be formed dynamically
  Essentially, it is SPMD programming model implemented on SIMD hardware

## Slide 90: SPMD
Single procedure/program, multiple data
  This is a programming model rather than computer organization
Each processing element executes the same procedure, except on different data elements
  Procedures can synchronize at certain points in program, e.g., barriers
Essentially, multiple instruction streams execute the same program
  Each program/procedure 1) works on different data, 2) can execute a different control-flow path, at run-time
  Many scientific applications are programmed this way and run on MIMD hardware (multiprocessors)
  Modern GPUs programmed in a similar way on a SIMD hardware

## Slide 91: SIMD vs. SIMT Execution Model
SIMD: A single sequential instruction stream of SIMD instructions  each instruction specifies multiple data inputs
  [VLD, VLD, VADD, VST], VLEN
SIMT: Multiple instruction streams of scalar instructions  threads grouped dynamically into warps
  [LD, LD, ADD, ST], NumThreads
Two Major SIMT Advantages:
  Can treat each thread separately  i.e., can execute each thread independently on any type of scalar pipeline  MIMD processing
  Can group threads into warps flexibly  i.e., can group threads that are supposed to truly execute the same instruction  dynamically obtain and maximize benefits of SIMD processing

## Slide 92: Threads Can Take Different Paths in Warp-based SIMD
Each thread can have conditional control flow instructions
Threads can execute different control flow paths
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B
C
D
E
F
A
G
Slide credit: Tor Aamodt

## Slide 93: Control Flow Problem in GPUs/SIMT
A GPU uses a SIMD pipeline to save area on control logic
  Groups scalar threads into warps
Branch divergence occurs when threads inside warps branch to different execution paths
Branch
Path A
Path B
Branch
Path A
Path B
Slide credit: Tor Aamodt
This is the same as conditional/predicated/masked execution.
Recall the Vector Mask and Masked Vector Operations?

## Slide 94: Remember: Each Thread Is Independent
Two Major SIMT Advantages:
  Can treat each thread separately  i.e., can execute each thread independently on any type of scalar pipeline  MIMD processing
  Can group threads into warps flexibly  i.e., can group threads that are supposed to truly execute the same instruction  dynamically obtain and maximize benefits of SIMD processing
If we have many threads
We can find individual threads that are at the same PC
And, group them together into a single warp dynamically
This reduces “divergence”  improves SIMD utilization
  SIMD utilization: fraction of SIMD lanes executing a useful operation (i.e., executing an active thread)

## Slide 95: Dynamic Warp Formation/Merging
Idea: Dynamically merge threads executing the same instruction (after branch divergence)
Form new warps from warps that are waiting
  Enough threads branching to each path enables the creation of full new warps
Warp X
Warp Y
Warp Z

## Slide 96: Dynamic Warp Formation/Merging
Idea: Dynamically merge threads executing the same instruction (after branch divergence)
  Fung et al., “Dynamic Warp Formation and Scheduling for Efficient GPU Control Flow,” MICRO 2007.
Branch
Path A
Path B
Branch
Path A

## Slide 97: Dynamic Warp Formation Example
A
A
B
B
G
G
A
A
C
C
D
D
E
E
F
F
Time
A
A
B
B
G
G
A
A
C
D
E
E
F
Time
A
x/1111
y/1111
B
x/1110
y/0011
C
x/1000
y/0010
D
x/0110
y/0001
F
x/0001
y/1100
E
x/1110
y/0011
G
x/1111
y/1111
A new warp created from scalar threads of both Warp x and y executing at Basic Block D
D
Execution of Warp x
at Basic Block A
Execution of Warp y
at Basic Block A
Legend
A
A
Baseline
Dynamic
Warp
Formation
Slide credit: Tor Aamodt

## Slide 98: Hardware Constraints Limit Flexibility of Warp Grouping
Lane
Functional Unit
Registers
for each
Thread
Memory Subsystem
Registers for thread IDs
0, 4, 8, …
Registers for thread IDs
1, 5, 9, …
Registers for thread IDs
2, 6, 10, …
Registers for thread IDs
3, 7, 11, …
Slide credit: Krste Asanovic
Can you move any thread
flexibly to any lane?

## Slide 99: Large Warps and Two-Level Warp Scheduling
Two main reasons for GPU resources be underutilized
  Branch divergence
  Long latency operations
time
Core
Memory
System
All Warps Compute
Req Warp 0
All Warps Compute
Req Warp 1
Req Warp 15
Round Robin Scheduling, 16 total warps
Narasiman et al., “Improving GPU Performance via Large Warps and Two-Level Warp Scheduling,” MICRO 2011.

## Slide 100: Large Warp Microarchitecture Example
Decode Stage
1
0
0
1
0
1
0
0
0
0
1
1
1
0
0
0
0
0
1
0
0
1
0
0
1
0
0
1
0
1
0
0
0
0
0
0
1
1
1
1
0
0
0
0
1
1
1
1
0
0
0
1
1
1
1
1
1
0
1
Sub-warp 0 mask
Sub-warp 0 mask
Sub-warp 1 mask
Sub-warp 0 mask
Sub-warp 1 mask
Sub-warp 2 mask
1
1
1
1
1
1
1
1
Reduce branch divergence by having large warps
Dynamically break down a large warp into sub-warps
Narasiman et al., “Improving GPU Performance via Large Warps and Two-Level Warp Scheduling,” MICRO 2011.
100

## Slide 101: Two-Level Round Robin
Scheduling in two levels to deal with long latency operations
Narasiman et al., “Improving GPU Performance via Large Warps and Two-Level Warp Scheduling,” MICRO 2011.
time
Core
Memory
System
All Warps Compute
Req Warp 0
All Warps Compute
Req Warp 1
Req Warp 15
Round Robin Scheduling, 16 total warps
time
Core
Memory
System
Compute
Req Warp 0
Req Warp 1
Req Warp 7
Two Level Round Robin Scheduling, 2 fetch groups, 8 warps each
Group 0
Compute
Group 1
Req Warp 8
Req Warp 9
Req Warp 15
Compute
Group 0
Compute
Group 1
Saved Cycles
101

## Slide 102: Improving Warp Scheduling
Veynu Narasiman, Chang Joo Lee, Michael Shebanow, Rustam Miftakhutdinov, Onur Mutlu, and Yale N. Patt, "Improving GPU Performance via Large Warps and Two-Level Warp Scheduling" Proceedings of the 44th International Symposium on Microarchitecture (MICRO), Porto Alegre, Brazil, December 2011. Slides (ppt) A previous version as HPS Technical Report, TR-HPS-2010-006, December 2010.
102

## Slide 103: We did not cover the following slides. They are for your preparation for the next lecture.

## Slide 104: An Example GPU

## Slide 105: NVIDIA GeForce GTX 285
NVIDIA-speak:
  240 stream processors
  “SIMT execution”
Generic speak:
  30 cores
  8 SIMD functional units per core
Slide credit: Kayvon Fatahalian

## Slide 106: NVIDIA GeForce GTX 285 “core”
…
= instruction stream decode
= SIMD functional unit, control
shared across 8 units
= execution context storage
= multiply-add
= multiply
64 KB of storage
for thread contexts (registers)
Slide credit: Kayvon Fatahalian
Notes: 30 * 32 * 32 = 30 * 1024 = 30K fragments
64KB register file = 16 32-bit registers per thread = 64B (1/32 that of LRB)
16KB of shared scratch
80KB / core available to software

## Slide 107: NVIDIA GeForce GTX 285 “core”
…
64 KB of storage
for thread contexts (registers)
Groups of 32 threads share instruction stream (each group is a Warp)
Up to 32 warps are simultaneously interleaved
Up to 1024 thread contexts can be stored
Slide credit: Kayvon Fatahalian
Notes: To get maximal latency hiding:
Run 1/32 of the time
16 words per thread = 64B

## Slide 108: NVIDIA GeForce GTX 285
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
30 cores on the GTX 285: 30,720 threads
Slide credit: Kayvon Fatahalian
Notes: If you’re running a CUDA program, and your not launching 30K threads, you are certainly not getting full latency hiding, and you might not be using the GPU well

## Slide 109: Evolution of NVIDIA GPUs

## Slide 110: NVIDIA V100
NVIDIA-speak:
  5120 stream processors
  “SIMT execution”
Generic speak:
  80 cores
  64 SIMD functional units per core
  Tensor cores for Machine Learning
NVIDIA, “NVIDIA Tesla V100 GPU Architecture. White Paper,” 2017.

## Slide 111: NVIDIA V100 Block Diagram
80 cores on the V100
https://devblogs.nvidia.com/inside-volta/

## Slide 112: NVIDIA V100 Core
15.7 TFLOPS Single Precision
7.8 TFLOPS Double Precision
125 TFLOPS for Deep Learning (Tensor cores)
https://devblogs.nvidia.com/inside-volta/

## Slide 113: Food for Thought
What is the main bottleneck in GPU programs?
“Tensor cores”:
  Can you think about other operations than matrix multiplication?
  What other applications could benefit from specialized cores?
Compare and contrast GPUs vs other accelerators (e.g., systolic arrays)
  Which one is better for machine learning?
  Which one is better for image/vision processing?
  What types of parallelism each one exploits?
  What are the tradeoffs?
Notes: Both concepts (GPUs and systolic arrays) can be combined in a heterogenous architecture.

## Slide 114: Computer Architecture Lecture 14: SIMD Processors and GPUs
Dr. Juan Gómez Luna
Prof. Onur Mutlu
ETH Zürich
Fall 2019
8 November 2019

## Slide 115: Clarification of some GPU Terms
Generic Term | NVIDIA Term | AMD Term | Comments
Vector length | Warp size | Wavefront size | Number of threads that run in parallel (lock-step) on a SIMD functional unit
Pipelined functional unit / Scalar pipeline | Streaming processor / CUDA core | - | Functional unit that executes instructions for one GPU thread
SIMD functional unit / SIMD pipeline | Group of N streaming processors (e.g., N=8 in GTX 285, N=16 in Fermi) | Vector ALU | SIMD functional unit that executes instructions for an entire warp
GPU core | Streaming multiprocessor | Compute unit | It contains one or more warp schedulers and one or several SIMD pipelines